## Slide 1
©KEMET Corporation. All Rights Reserved.
SCF39XV & SCR39XV & SCT39XV Line Filters
AUTOMOTIVE GRADE COMMON MODE CHOKES
On board charger
Electric compressor
Electric heater
Starter booster
Applications
Benefits
DC / DC converter
Electric oil pumps
Electric power steering
WPT systems
Overview
Horizontal layouts and three different core materials (nanocrystal, ferrite S15H & ferrite 7HT)
Rated current range: 10 A to 50 A
Inductance range: SCF39XV 0.22 to 19.5 mH | SCR39XV 0.11 to 10.3 mH | SCT39XV 0.067 to 5.85 mH
DCR: 0.4 to 17.9 mΩ
Operating temperature: SCR39XV -40°C to +120°C | SCF39XV & SCT39XV -40°C to +150°C
Selection Guide
Electrical Characteristics
Proprietary S15H or 7HT ferrite material or high permeability nanocrystal material
Rated voltage up to 1,000 V AC/DC
High impedance
High inductance
UL 94 V–0 flame retardant rated base and cap
AEC-Q200 qualified
IATF 16949 managed
Customized standard parts
SCF | 39 | XV- | 120- | S | 1R5 | A | 017 | JH
Series | Outer Core Diameter | Approval | Rated Current | Phase | Wire Diameter | Windings | Number of Turns | Terminal Base Type
SCF = Nanocrystal core SCR = S15H ferrite core SCT = 7HT ferrite core | 39 = 39 mm ø | XV = AEC-Q200 | 120 = 12 A | Blank = Single-phase S = Three-phase Y = Three-phase four-wire Z = Three-phase four-wire asymmetric | 1R5 = 1.5mm ø | A = Single B = Double | 017 = 17 turns | JH = Horizontal
Part Number System
SC39XV
Single-Phase
SCF39XV, SCR39XV & SCT39XV common mode chokes have 105 parts, consisting of horizontal layouts in a core size of 39 mm and three types of core material combinations, allowing the selection of the suitable specification for each application. It has a withstand voltage of 1,000 V AC/DC to meet the higher voltage requirements of automotive batteries.
SC39XV-S
Three-Phase
SC39XV-Y
Three-Phase Four-Wire
SC39XV-Z
Three-Phase Four-Wire
(Asymmetric Type)
Chart: Rated Current (A)
| 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 27 | 28 | 29 | 30 | 31 | 32 | 35 | 40 | 42 | 44 | 50
SCF39XV | 19.5 | 14.4 | 12.1 | 9 | 7.2 | 5.6 | 4.9 | 4.2 | 3.6 | 3 | 1.2 | 0.9 | 0.62 | 0.4
SCR39VX | 10.3 | 7.6 | 6.4 | 4.8 | 3.8 | 3 | 2.6 | 2.23 | 1.9 | 1.6 | 0.64 | 0.47 | 0.33 | 0.21
SCT39XV | 5.85 | 4.3 | 3.6 | 2.7 | 2.16 | 1.68 | 1.46 | 1.26 | 1.07 | 0.9 | 0.364 | 0.268 | 0.187 | 0.119
SCF39XV-S | 7.2 | 4.9 | 3 | 2 | 1.6 | 1.2 | 0.9 | 0.22
SCR39XV-S | 3.8 | 2.6 | 1.6 | 1.07 | 0.84 | 0.64 | 0.47 | 0.118
SCT39XV-S | 2.15 | 1.46 | 0.9 | 0.6 | 0.476 | 0.364 | 0.268 | 0.067
SCF39XV-Y | 1.6 | 1.2 | 0.9 | 0.62 | 0.4 | 0.23
SCR39XV-Y | 0.84 | 0.64 | 0.47 | 0.33 | 0.21 | 0.118
SCT39XV-Y | 0.476 | 0.365 | 0.268 | 0.187 | 0.119 | 0.067
SCF39XV-Z | 3.6 | 2.5 | 2 | 1.6 | 1.2 | 0.62 | 0.4
SCR39XV-Z | 1.9 | 1.31 | 1.06 | 0.84 | 0.64 | 0.33 | 0.21
SCT39XV-Z | 1.07 | 0.744 | 0.6 | 0.476 | 0.365 | 0.187 | 0.119